## Slide 2: RUNWAY MONITORING AT SBCF Implementing GRF and Drones for Enhanced Safety and Operational Efficiency

## Slide 3: Agenda
Part I - Implementing GRF
Understanding the Implementation
Inspection Procedure between ATC and OPS
GRF Inspection
Key Points
Part II - Runway Monitoring Using Drones
Implementation of Drone Procedures
Runway Inspections Using Drones

## Slide 4: Part I - Implementing GRF

## Slide 5: Understanding the Implementation
Historical Analysis of Slippery Runway Reports in SBCF
Examination of Meteorological Conditions on the Day of Reporting
Analysis of TAF/METAR/SPECI Data
Determination of Triggers Based on Historical Reports
Current Rain Intensity (15mm/h)

## Slide 6: Inspection Procedure between ATC and OPS
TWR-CF
INITIATES CALL TO APOC-BHA
Activation via phone or radio once the rainfall index reaches 15 mm/h or after two consecutive reports of slippery runway or poor RBA conditions..
REQUESTS INSPECTION FROM THE ON-DUTY GRF TEAM
GRF TEAM - CONDUCTS MEASUREMENTS AT WATER ACCUMULATION POINTS IN EACH THIRD OF THE RUNWAY
TWR-CF prepares air traffic planning for the coordination of the inspection.
After each measurement of 1/3 of the runway, the GRF team immediately informs APOC.
APOC-BHABEGINS THE RWYCC EVALUATION AND REPORTS THE INFORMATION TO TWR-CF
GRF team returns to APOC and provides complete information about the runway conditions, publishing RWYCC in the system.

## Slide 7: GRF Inspection
WHAT TO OBSERVE DURING THE INSPECTION:
Identify the contaminated thirds of the Runway 16/34.
Type of contaminant.
Quantity of the contaminant.
Areas of water accumulation (puddles or water sheets).
Ruler to Measure Contaminant Depth

## Slide 8: Key Points:
1. Worst-Case Scenario Consideration:
  Always consider the worst-case scenario.
  If 1/3 of the runway is rated as 5 or 3, we will consider the entire runway as 5/5/5 or 3/3/3.
2. Visual Inspections:
  Predominantly visual inspections due to more than 160 consecutive days without rainfall.
3. Runway Pavement Construction:
  Pavement design is favorable for preventing contaminant accumulation and promoting efficient water drainage.
4. Inspection Triggers:
  Trigger is activated only after a poor RBA report and when the runway is wet.
  Slippery runway reports during dry conditions will not trigger a GRF inspection, but rather a routine inspection.

## Slide 9: Part II - Runway Monitoring Using Drones

## Slide 10: Implementation of Drone Procedures
ICA 100-40
OPERATIONAL AGREEMENT BH AIRPORT & DTCEA CF
AIRPORT SAFETY RISK ANALYSIS

## Slide 11: Runway Inspections Using Drones
With drone technology, we can assess the following aspects of runway conditions:
Pavement Conditions: Detection of cracks, surface degradation, and other structural issues.
RESA (Runway End Safety Area) Conditions: Monitoring the state of safety areas at the runway ends.
Runway signs and markings Conditions: Verification of the integrity and visibility of runway signs.
Runway Shoulders Conditions: Inspection of the conditions along the edges of the runway.
Lighting System Conditions: Assessment of the state and functionality of runway lights.

## Slide 12: Runway Inspections Using Drones

## Slide 13: Runway Inspections Using Drones