## Slide 1: Building capacity for long-term energy plans: factoring market design aspects
Long-term Scenarios for the Clean Energy Transition in Latin America
25-26 February 2019, Brasilia, Brazil
Bernardo Bezerra bernardo@psr-inc.com

## Slide 2
Our team has 60 people with degrees in optimization, energy systems, statistics and computer science
(17 PhDs, 31 MSc)
We work in more than 80 countries in all continents

## Slide 3: Planning procedure with renewable sources
Co-optimization of generation, reserve and interconnections
Probabilistic hourly simulation of system operation and supply reliability evaluation
Detailed probabilistic transmission and VAr planning
Optimal Power Flow (linearized active power and full AC models)
Inventory of hydro basins and other renewable resources
Multiscale stochastic scenarios (inflows, renewables etc.)
Distributed processing
Modeling of renewable generation (hydro, wind, solar etc.), storage (batteries, fuel etc.), thermal plants (gas, coal, nuclear), demand response, power transmission and gas networks, distributed generation

## Slide 4: Different areas of knowledge are required
Project inventory
Project engineering
Data analysis
Uncertainty mapping
Data analysis
Stochastic modeling
Building scenarios for exogenous variables
Macroeconomics
Geopolitics
Social and environmental analysis
Economic evaluation
Data analysis
Power sector modeling
Optimization
Power engineering
What-if scenarios
However, each country has its unique market design, which affects the long-term scenarios for Clean Energy Transition

## Slide 5: Market design impact on long-term scenarios do Clean Energy Transition
LCOE
Expansion Optimization
Multistage Mixed Integer Optimization
CAPEX
OPEX
WACC
Spot prices remunerate LCOE
Long-term scenario for “energy only” market design
LCOE
Expansion Optimization
Multistage Mixed Integer Optimization
CAPEX
OPEX
WACC
Spot prices does not remunerate LCOE
Long-term scenario for multi-products market design
Other services
(e.g. frequency control)
Other revenues

## Slide 6: Factoring market design aspects
Understand the regulatory framework and market design of the country
Identify products that correspond to revenue streams for the market agents
  Example: in some jurisdictions batteries are built for frequency control, but affecting the energy market.
Identify country targets for each product
Identify market design mechanism to contract each product
Identify market design flaws or loopholes
  Different market design assumptions can be used to prepared different long-term scenarios
  Long-term scenarios can be used to address market design flaws
Mapping market design aspects into mathematical constraints for the computational model

## Slide 7: Example: Brazil
Expansion driven mainly by auctions in the regulated market
Consumers obliged to be 100% contracted in terms of firm energy
Distribution companies contract 103% of the demand for growth uncertainty hedge
Impact of market design on expansion mix:
Chart: MW
| Natural Gas | Nuclear | Solar | Biomass | Hydro | Fuel/Diesel Oil | Wind
without Physical Guarantee Restriction | 6224.9548 | 2400 | 0 | 8810 | 0 | 0 | 20250
with Physical Guarantee Restriction | 6361.3448 | 2400 | 0 | 17620 | 0 | 0 | 20250
Chart: Expansion Capacity for 2035 without Physical Guarantee restriction
| Natural Gas | Nuclear | Solar | Biomass | Hydro | Fuel/Diesel Oil | Wind
w/o PhG | 0.16518 | 0.063686 | 0 | 0.23378 | 0 | 0 | 0.53735
Chart: Expansion Capacity for 2035 with Physical Guarantee restriction
| Natural Gas | Nuclear | Solar | Biomass | Hydro | Fuel/Diesel Oil | Wind
w/ PhG | 0.13642 | 0.051468 | 0 | 0.37786 | 0 | 0 | 0.43426

## Slide 8: Example: Colombia
Expansion driven by reliability call option auctions
Target: 100% of demand backed up by firm energy
Impact of market design on expansion mix:

## Slide 9: Example: México
Expansion driven by auctions for Energy, Capacity and Clean Energy Certificates
System-wide targets for Clean Energy Certificates and Capacity
Evolution of prices for different products:
Expansion plan
Energy prices
Capacity prices
CEL prices
Project feasibility

## Slide 10: Conclusion
Energy transition poses new challenges for model-based scenario development…
  Higher spatial and time granularity
  Higher coordination between transmission and generation expansion
  Higher data volume
…which needs jointly efforts from different fields of expertise.
  Data analysis, stochastic optimization, project engineering, social and environmental analysis, economic evaluation, macroeconomics, geopolitics, etc.
Higher penetration of renewables also poses new challenges for market design, which affects model-based scenario development
  Each country has its owns products and contracting mechanisms
Expertise in market design is essential for building long-term scenarios closer to reality
Long-term scenarios can also be used to identify market design improvements for a secure, sustainable and affordable energy transition

## Slide 11: Thank You